## Slide 2
Practical Clustered Shading Ola Olsson – Chalmers University of Technology
Emil Persson – Avalanche Studios

## Slide 3: Overview
Part 1
  Introduction to Clustered Shading
  Ola Olsson – Chalmers University of Technology
Part 2
  Practical Implementation at Avalanche
  Emil Persson – Avalanche Studios
Notes: This is the first part of the two part presentation about practical clustered shading. The first part is presented by Ola Olsson, PhD student at Chalmers University of Technology, and covers the motivation, introduction and background to clustered shading. The second part, by Emil Persson, head of research at Avalanche Studios, deals with the reasons and adaptions to put the technique into production in the open-world engine at Avalanche.

## Slide 4: Clustered Shading
“Clustered Deferred and Forward Shading”
Olsson, Billeter, Assarsson
HPG 2012
Extends Tiled Shading
Notes: Clustered Shading, was first introduced by myself and co-authors in a paper published at the Hight Performance Graphics conference 2012. The algorithm builds on, and extends, tiled shading.

## Slide 5: Clustered Shading – Summary
Real-time shading
  Thousands of lights
    Limited range lights
    No shadows
  Fully dynamic
    Lights and Geometry
Robust performance
  Low overhead
  Low view-dependence
  Handles noisy depth distributions
    Even transparency
  Can scale to 1M lights.
Falloff
Influence = 0
Influence = 1
Light Range
Notes: Our algorithm targets thousands of lights in real time,
The lights have a limited range, with some falloff which goes to 0 at the boundary.
This means that lights are not physical, and the scaling with increasing light range is an interesting direction of future work.
We further do not consider shadows, also interesting for future work!
There is no pre-computation, so all geometry and lights are allowed to change freely from frame to frame.
Our evaluation shows that the algorithm
Can be implemented with low overhead
View dependence is low, meaning performance can be robustly predicted from scene complexity.
Can support depth distributions with a lot of noise, i.e. many discontinuities, and also transparency where several depth layers are present.
We show that clustered shading can scale to at least 1M lights, showing the number of lights is not a fundamental limitation
More important at this point is what to do with all these lights!

## Slide 6: Why More Lights?
Global Illumination
  Virtual Point Lights
  Photon Splatting
Complex Lights
  Area / Volume
Photon Splatting, 739k photons [2]
Notes: To answer this question I’ve selected a few examples
The first is that it could be used to visualize the result of global illumination simulations
Many lights can be used for virtual point lights, but also photon splatting can use a very similar implementation.
We can also use more lights to emulate complex light types

## Slide 7: Why More Lights?
Artistic Freedom
  Lighting design.
Need For Speed: The Run, ~2600 lights [1]
Notes: We can also let the artists design the light environment with greater freedom,
As in this example from need for speed the run, which uses many lights to get a GI look

## Slide 8: Why More Lights?
Dynamic Effects
  Explosions
  Particle Effects
  Laser
  Torches
  Etc.
Starcraft 2 [Blizzard 2010]
+25
lights
Notes: Finally there are many things in games that ought to light up the environment, but doesn’t always
In this example only the big thingo here is a light
All the muzzle flashes are just billboards,
Turning them into lights would add another 25 lights to this scene.

## Slide 9: Many Lights – Light Assignment
Lights vs. visible geometry
Hundreds to thousands of lights
Lots of complex geometry
Notes: The key problem we are trying to address in our paper and in this talk is how to figure out which lights affect what geometry.
This becomes difficult when we are dealing with thousands of lights and lots of complex geometry.
So, while the technique is called “clustered shading” for historical and contextual reasons going back to deferred shading and tiled shading, a more precise name might have been ‘Clustered Light Assignment’. We will however persist in calling it clustered shading for consistency with published work.

## Slide 10: Many Lights – Light Assignment
Previous Solutions
  Traditional – per object
  Deferred Shading – per pixel
Modern Solutions
  Tiled Shading – per pixel tile
  Clustered Shading – per 3D tile
Notes: Older solutions have solved this either on a per object basis, which has a lot of inherent problems, such as the conflict between optimizing batch size for drawing and minimizing light influences (consider a long and skinny bit of geometry with few polygons.
or per pixel, as in deferred shading, which typically is a bandwidth limited process on modern hardware.
Modern solutions attain higher performance by working on groups of pixels.

## Slide 11: Example Scene
Crytek Sponza
  Minus top
6 Lights
A Tree
Notes: We will be using this example scene to illustrate how tiled and clustered shading works.
The scene is the usual Crytek Sponza scene, but with the top three quarters lifted off, to let us get a better view.
I’ve added six lights of different colours, represented as spheres.
To make the view more interesting, I’ve also added a tree.

## Slide 12: Example Scene
Crytek Sponza
  Minus top
6 Lights
A Tree
Notes: The same view in outline mode, to make it more clear.

## Slide 13: Example Scene
Crytek Sponza
  Minus top
6 Lights
A Tree
Notes: This is the viewpoint that will be used to demonstrate the algorithms, the camera is looking through the tree towards the lion head on the wall.

## Slide 14: Example Scene
Notes: Shifting to the point of view of the yellow camera.

## Slide 15: Tiled Shading Recap
Deferred or Forward*.
Simple.
Fast (sometimes).
2D
* Which AMD calls “Forward+”
Notes: Now I will go into a re-cap of how tiled shading works.
Tiled shading can be implemented using either deferred of forward shading techniques, or a mix. Note that AMD insists on calling “Tiled Forward Shading”, “Forward+”, it is however identical.
For light assignment, it matters very little which form we use, so I will not go into specifics.
It is conceptually very simple, and also relatively easy to implement, at least in the simplest form.
Performance is good, given the right circumstances.
And fundamentally it is a 2D algorithm.

## Slide 16: Tiled Shading Recap
Screen space tiles
  E.g. 32x32 pixels
  Each contains list of lights
Notes: Tiled Shading works like this.
The screen is divided into tiles, each covering say 32 by 32 pixels.
Each tile contains a single list of all the lights that might influence any of the pixels inside.
Note that this list is shared between the pixels, so overhead for list maintenance and fetching is low.

## Slide 17: Tiled Shading Recap
For each Light
  Find screen space AABB
Notes: To construct the lists, we might do as follows.
For each light, establish the screen space bounding box, illustrated for the green light.

## Slide 18: Tiled Shading Recap
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
For each Light
  Find screen space AABB
  Add light to affected tiles
Notes: Then add the index of the light to all of the overlapped tiles.

## Slide 19: Tiled Shading Recap
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Notes: Then repeat this process for all remaining lights.

## Slide 20: Tiled Shading Recap
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
2
1
2
1
2
1
2
2
2
2
2
2
2
2
2
1
1
1
1
1
1
1
2
1
2
2
2
1
1
1
1
1
1
1
1
1
1
1
2
2
2
2
2
2
2
2
2
2
2
1
2
Notes: The illustration only shows the counts, so you need to imagine the lists being built as well.
In practice we’d also do a conservative per-tile min/max depth test, to cull away lights occupying empty space.

## Slide 21: Tiled Shading Recap
Shading pass
  Deferred or Forward
For each sample
  Loop over list of lights
Notes: Once all the lists are constructed, a shading pass is performed.
For tiled deferred shading, it is a deferred full screen pass.
For tiled forward shading, it is a geometry pass.
In each case the light list is looked up using the fragment coordinates and looped through and shading is accumulated.

## Slide 22: Tiled Shading
Notes: This is a view of the tile geometry pulled out of our implementation.

## Slide 23: Tiled Shading
Notes: Switching to the overhead view, we see how they extend from the tree over to the background geometry.

## Slide 24: Tiled Problems
Tiles – 2D
Games – 3D
  Hmm…
Notes: Toggling on the light geometry, we see that there is a lot of overlap…
…even in the empty space behind the tree.
We now should be able to start seeing the shape of the problem with 2D tiles in a 3D world.

## Slide 25: Tiled Problems
Single Tile
Notes: We’ll now take a closer look at a single tile, in order to highlight the problem.

## Slide 26: Tiled Problems
Single Tile

## Slide 27: Tiled Problems
Single Tile
Notes: As we can see, there is a small number of samples from the tree
And the rest, the lion share of the pixels are in the background.

## Slide 28: Tiled Problems
Notes: * In 3D the tile looks like this…

## Slide 29: Tiled Problems

## Slide 30: Tiled Problems
Intersects all 6 lights
Notes: Extending from the tree through the visible scene to the wall.
This one troublesome tile intersects all 6 lights in our simple test scene.

## Slide 31: Tiled Problems
Intersects all 6 lights
Notes: While actually some of the samples, from the tree, are affected zero of these lights.

## Slide 32: Tiled Problems
Intersects all 6 lights
Notes: And the rest, would only need two of the lights.

## Slide 33: Tiled Problems
Tiles – 2D
Geometry Samples – 3D
  Fragments / Pixels
Light density – 3D
View dependent
  Unpredictable shading times
Notes: So as we have shown, there is a fairly fundamental problem with tiled shading.
The basic problem stems from that we are making the intersection between lights and geometry samples, both of which are 3D entities, in a 2D screen space.
The main practical issue with this is that the resulting light assignment is highly view dependent. This means that we cannot author scenes with any strong guarantee on performance, as a given view of the scene may have a significantly higher screen space light density than average.
For example, we’d like to be able to construct a scene with, say, maximum 4 lights affecting any part of the scene. In this case, we would like shading cost to be proportional to this, and stable, given different view points. Unfortunately, no such correlation exists for tiled shading.
In other words shading times are unpredictable, which is a major problem for a real time application.

## Slide 34: Clustered Shading - Key Idea
Add the 3rd dimension
  Tile also in depth direction = cluster
  Also > 3 dimensions (e.g. normals)
hk
dk=hk
Z
Y
neark
fark
near
far
Notes: So how do we solve this?
This is the basic question for our clustered shading paper.
A fairly obvious solution, given what has been said so far, is to use 3D tiles of some sort.
It is less obvious what particular kind of subdivisions to use, and whether this will actually improve efficiency.
Another question we explore in the paper is to tile in yet higher dimensions, based on normal direction as well.

## Slide 35: Clustered Solutions
Notes: Compare the tiles show here…

## Slide 36: Clustered Solutions
Notes: …with the view space cluster AABBs shown here.
Along the top edge of the screen, it is easy to see that the clusters and tiles are very similar, where the depth within each tile is shallow.
In the middle, where the tree is, things are more interesting, as several layers of depth are visible.

## Slide 37: Clustered Solutions
Notes: Going to the overhead view again.

## Slide 38: Tiled Problems
Notes: Comparing the tiles…

## Slide 39: Clustered Solutions
Notes: …to the clusters, shows that the clusters approximate the visible geometry a lot better.
This means that the intersection with the light volumes ought to also be more precise.

## Slide 40: Clustered Solutions
Notes: Going back to the single tile example, but with clusters.

## Slide 41: Clustered Solutions
Notes: Except that there are several clusters instead of a single tile now.

## Slide 42: Clustered Solutions
Clusters – 3D
Games – 3D
  Yay
Notes: …

## Slide 43: Tiled Problems

## Slide 44: Tiled Problems
Intersects no lights
Notes: We see that none of the lights overlap the clusters that are on the tree in the fore ground.

## Slide 45: Tiled Problems
Intersects 2 lights
Notes: And in the background, only the volumes of the two required lights intersect.
Clearly clusters has a good potential for improving efficiency, we’ll now need to talk about how they can be implemented.

## Slide 46: Clustered Shading – Algorithm
Rasterize G-Buffers
  Forward: pre-z pass
Cluster assignment
Find unique clusters
Assign lights to clusters
Shade view samples
  Deferred: Full screen pass
  Forward: Geometry pass
Notes: This is a high level version of the clustered shading algorithm
I’ve grayed out parts that are identical to tiled shading.
Cluster assignment means to identify what cluster each sample belongs to, this is a simple mapping.
Then we need to work out which of the clusters are represented by these samples, and
Finally we assign lights to these clusters, ensuring we are not wasting storage and work assigning lights to empty clusters.
Note that Emil will be presenting a rather different approach to implementing the algorithm, which leaves out and replaces the first two steps.

## Slide 47: Cluster Assignment
Cluster key:
  ck = (i, j, k) integer tuple
i, j = 2D tile id
  gl_FragCoord.xy
k = log(view space z)
hk
dk=hk
Z
Y
neark
fark
near
far
Eye
Notes: Cluster assignments is a simple mapping from sample coordinate, to an integer tuple i,j,k
  i and j are simply the tile coordinates, which can be derived by dividing gl_FragCoord.xy by the tile size.
k is a logarithmic function of the view space Z of the sample, not simply the logarithm, for the exact equation see the paper.
We use this subdivision as it creates self similar clusters that are as cube like as possible. This makes them better suited for culling. The logarithmic subdivisions also means that as clusters become larger further away, we get a kind of LOD behaviour and do not end up with insane numbers of clusters, for a wide range of view parameters.

## Slide 48: Finding Unique Clusters
Full screen pass.
Flag used clusters.
  Read depth
  Compute ck
  Set cell in grid to one.
Forward:
  Geometry pass with side effect.
Z
Y
near
far
Eye
Notes: Finding the unique clusters is a full screen pass, which simply constructs the cluster key for each sample.
And sets the corresponding cell in a 3D grid to 1. This grid is non-regular subdivision of the view volume.

## Slide 49: Finding Unique Clusters
Z
Y
near
far
Eye
Compact Non-Zero
  Yields list of non-empty clusters.
Parallel prefix sum
  chag::pp (CUDA)
  thrust (CUDA)
  Compute Shader API?
1
2
4
5
6
7
32
33
34
39
Notes: We then compact the grid into the list of non-zero elements.
This can be implemented through a parallel perfix sum.
Which is a very quick process, for the million elements or so needed.
  Taking a fraction of a millisecond.
This leaves us with a list of clusters which needs lights assigned to them.

## Slide 50: Light Assignment
Many clusters
Many lights
Hierarchical approach
  Hierarchy over lights
    32-way tree (matches SIMD of GPU)
    Dynamically rebuilt on GPU
  Each cluster traverses light tree
    BV tests
Notes: When pushing the limit on number of lights, a hierarchy over lights makes sense.
We use a BVH with a branching factor of 32, which is rebuilt each frame.
When not so many lights are used, there are many other approaches which may be better. Again Emil will show a rather different approach later on.

## Slide 51: Results
Crytek Sponza
  +Trees
  10k Lights
Tough on Tiles
Notes: So for some results.
This is the good old crytek sponza scene again, but this time with 3 trees added, and 10 thousand lights.
This is a pretty difficult scene for tiles, and we use it to highlight where the algorithm breaks down.
It is, however, not a completely outrageous case, with large areas of coherent pixels, and a moderate number of lights if global illumination effects are considered.

## Slide 52: Results (GTX 480) Sponza + Trees
Chart: Time (ms)
| TiledDeferred | ClusteredForward | ClusteredDeferredPt | ClusteredDeferredEbEn | ClusteredDeferredNk3 | ClusteredDeferredNk3EbEn
Deferred Render | 3.1998 | 0.9548 | 3.1916 | 3.1909 | 3.2107 | 3.1962
Find Unique Clusters | 0 | 0.8125 | 0.8128 | 3.1022 | 3.1214 | 5.1436
Light Assignment | 3.4221 | 2.2752 | 2.2741 | 2.5858 | 7.8047 | 7.2907
Shading | 10.9615 | 7.0909 | 3.6932 | 2.8359 | 3.0189 | 2.4098
Tiled
Deferred
Clustered
Forward
Clustered
Deferred
Clustered
Explicit
Clustered
3x3 Normals
Clustered Explicit
3x3 Normals
Notes: As seen here, tiled shading is dominated by shading time, even for our quite simple pixel shader.
This means that improving speed of the tiling would ot change the result much.
Clustered shading, on the other hand, is more balanced between shading and other parts of the algorithm.
Also shown are three variants with more complex culling based on normals as well. These do not pay off in our implementation as the reduction of shading cost is overtaken by the cost of more complex culling and a greater number of clusters.
With more expensive shading and better implementation of clustering and culling, they might still be worhtwhile.

## Slide 53: More Results
Discontinuities
View from Camera
3D bounds for Tiles
- Unreal 3 Scene
  ‘Necropolis’
- Tricky view
  But not artificial
2D tiles with depth bounds
High light density
  Around 2000 lights
Notes: This is a view from the scene Necropolis included in the UDK (Unreal SDK).
We have added a few thousand dynamic lights (shown as lovely GLUT solid spheres), to spice things up.
The tile bounds shown to the right, are as horrible as we might expect.

## Slide 54: More Results
Discontinuities
# Lights / Tile
Black = zero
Green ~ 150
White > 300
Tiled: 18.8ms
Clustered: 9.4 ms
3D bounds for Tiles
Notes: And the performance, follows.
In the white parts there are more than 300 lights for each sample.
Tiled Deferred Shading clocks in at 18.8 ms per frame.
Clustered, almost exactly half that time.

## Slide 55: More Results
Discontinuities
# Lights / Tile
Black = zero
Green ~ 150
White > 300
Tiled: 18.8ms
Clustered: 9.4 ms
3D bounds for Clusters
Notes: Looking at the heat map, clustered shading tops out at around 100 lights per sample, so there is still some pretty dense lighting going on out there.
As we can see to the right, the clusters match the geometry that much better.

## Slide 56: Tiled Forward Shading [4]
near
Eye
Z
Y
far
Transparent Geometry
Problem
  View dependent
  Degenerates to 2D
  Full screen discontinuity!
Notes: Talking briefly on what happens when we add transparent geometry to the mix.
In tiled shading, the result of transparent geometry covering the view is effectively the loss of the depth range optimization
  which has been shown to lead to poor performance.
Again, the biggest issue here is that it is view dependent, and so will only be possible to determine at run time
  and, as we all know, this kind of problem usually starts showing up five minutes after we shipped a build to the publisher.

## Slide 57: Clustered Forward Shading [4]
Z
Y
near
far
Eye
Pre-geometry pass.
Flag used clusters.
  Side effect in fragment shader.
  Set cell in grid to one.
Notes: Clustered Shading does not suffer from this problem, as each cluster represents a fixed section of 3D space.
The only problem we face is trying to determine what clusters are need such that we can assign lights to them.
This can be done by rendering a pre-pass with the transparent geometry.
This can be performed after a regular G-buffer or pre-z pass, with color and depth writes turned off, and sets the used clusters to one as a side effect in the fragment shader.
The algorithm is otherwise as before.
Note that clustered shading provides an efficient way to solve the light assignment problem for any transparency technique, not just good old order dependent transparency.

## Slide 58: Clustered Forward – Performance
Crytek Sponza
  + Transparent Bubbles
1k Lights
CSAA
2.2x Overdraw
Notes: Now lets look at some runtime frame rates, measured on a GTX 580 gpu

## Slide 59: Clustered Forward – Performance
Tiled Deferred
Edge Detection
  Single sample shading
No Overdraw
  Deferred = Single layer
Notes: First let me point out that the measures for deferred does not include the transparent geometry.
So it is not a completely fair comparison.
Also, the implementation only shades all samples at discontinuities, As proposed by Lauritzen 2010. Therefore, most of the pixels in this view are computing the shading for just a single sample.

## Slide 60: Clustered Forward – Performance
1024 lights
CSAA
Clustered
  125 to 142 FPS
Tiled
  66 to 217 FPS
Chart: FPS, GTX 580
| 1 | 2 | 4 | 8 | 16
Tiled Deferred | 217.3913 | 181.8182 | 142.8571 | 111.1111 | 66.6667
Clustered Forward | 142.8571 | 142.8571 | 133.3333 | 133.3333 | 125
Tiled Forward | 90.9091 | 76.9231 | 71.4286 | 62.5 | 50
Tiled Deferred Eq | 96.9437 | 81.0802 | 63.7059 | 49.549 | 29.7294
Notes: So forward shades 2.2 times more samples for this view.
Despite this we see that Clustered Forward outperforms Tiled Deferred at high MSAA levels.
The dashed red line shows tiled deferred scaled to account for the difference in samples shaded.
In this case we see that clustered shading is far more efficient.
Also worth noting is that scaling with increasing MSAA levels is much better for the forward shading techniques.

## Slide 61: Clustered Shading - Summary
High performance
Low view dependence
Good worst-case performance
Fully Dynamic
Supports transparency
Forward / Deferred, or both
Practical?
  Let’s ask Emil

## Slide 62: References
[1] Multi-Image Based Photon Tracing for Interactive Global Illumination of Dynamic Scenes, Yao et. al. 2010
[2] Deferred shading techniques using frostbite in "Battlefield 3" and "Need for Speed the Run“, Ferrier and Coffin. 2011
[3] Clustered Deferred and Forward Shading, Olsson et.al. 2012
[4] Tiled and Clustered Forward Shading, Olsson et.al. 2012
Demo implementation with source: http://www.cse.chalmers.se/~olaolss

## Slide 63: The Cluster Advantage
Fast voxelization of samples
  Shadows?!
  Starting points for cone tracing?
  Approximate shading?
  Adaptive shading?
  Other uses?